## Slide 1
Chapter 2.10
Negotiating, Bidding and Buying the Job

## Slide 2
Must define all referenced documents
Well-developed contracts aid claims management
Contracts document precise agreements – must be highly accurate

## Slide 3
An agreement on scope, time and cost
Agreement on rules and procedures
Must conform to existing laws and accepted conventions in project area
Impossible, grossly inequitable, or illegal requirements are not enforceable
Contracts define the parties’ agreements about project

## Slide 4
Contractor not required to detect and correct all design errors
Schedule delay can have many causes and responsible parties
Forced work without agreed compensation is poor claim management
Some concealed conditions must be handled as claims (unforeseen conditions)
Fair and balanced contract terms produce best results

## Slide 5
Elements of the Contract

## Slide 6
Project name from initial contract documentation
Street address, building designation, location within multi-story building
Parties by their common legal name
  Or by their exact project specific name, e.g. a joint venture
Project and parties must be defined accurately – extreme precision not required

## Slide 7
General and special conditions outlined by contract
CM’s can add much meaningful definition to GC’s
Permanent building defined by drawings and specifications
May include surveys, test reports, and narratives
Scope: temporary work and the permanent building

## Slide 8
Specific work – defined configuration, grade and methods most common
Specific performance – riskier, trickier and less common
Evidence of successful completion must be well defined
Conventional well-known documents are preferred evidence
Specific work or performance achieved
may be required

## Slide 9
Parties’ rights and responsibilities defined
Rules for starting and stopping, changes in work, payment and schedules
Insurance, bonds, warrantees specified
Model contract GCs establish rules and limits

## Slide 10
General contractors and CMs responsible for temporary construction
Chosen temporary methods can hugely impact schedule and cost
Architect specifications address temporary methods lightly and carefully
Full definition can make architects responsible for inspection and liable for performance
GC’s discuss, but do not define, construction means and methods

## Slide 11
Design-bid-build produces a fixed contract sum
CM usually fixes a GMP (guaranteed maximum price)
Alternate costs and unit costs can add clarity to later refinements
Cost is usually clearly defined in contract

## Slide 12
Prior to award, time is usually not carefully calculated before transferring project out of preconstruction department
  Rules of thumb and intuitive judgment frequently used
Claims for changes in time difficult to present and prove, especially after they have already happened
  Time considerations must be communicated with owner changes as well, but owner may not be able to extend time so it is expected that the change includes overtime
Time is defined, but frequently with little analysis

## Slide 13
Developed by associations representing all contract parties
Carefully constructed and ultimately tested by litigation
AIA documents
  A101 – Standard Form of Agreement Between Owner and Contractor
  A201 – General Conditions of the Contract for Construction
AGC documents available, but less common
Standardized suites of documents are common and effective

## Slide 14
Work Packages Allocate Tasks, Management and Risk

## Slide 15
Communicating scope, time and cost - Sample
Assigning scope components to subs and vendors
  GC ultimately responsible to ensure all scope is complete, regardless of transference of scope to others
Providing facilities and services to benefit all
  Portable toilets, dumpsters, jobsite access, etc.
Directing, monitoring and controlling
Construction managers lead by:

## Slide 16
Subs have assembled organizations and established procedures that may also be incorporated into the specifications
Competencies by type of work or project, and size are narrow
  Keep work packages within subs’ “normal and customary” for best results, Don’t have mason bid electrical, etc.
Keep subcontractor work packages within their “comfort zone”

## Slide 17
Framing and drywall, acoustical tile ceilings, painting
Work packages must be normal and customary
for 3 or more bidders
  If you were planning on using subs that do work in other areas that you have used before, make sure they are able to meet the same scope demands or potentially be able to partner with another subcontractor.
Successful work packages are normal
and customary for project area

## Slide 18
Notification, notice to proceed, substantial completion, final completion
Force majeure, no damages for delay, liquidated damages
Prompt payment, pay when paid or pay if paid
Common contract terms must be learned well and understood

## Slide 19
Bidding and Buying the Job

## Slide 20
Invitation to bid or RFP (request for proposal)
Pre-bid conference followed by questions and answers
Proposals received and analyzed
Contract award
Proposals are solicited and reviewed

## Slide 21
Bid: precisely structured response to an exact set of instructions
Bid disqualified by exceptions, qualifications or imperfections
Voluntary alternates and beneficial suggestions welcomed
Bids very formal and proposals less formal

## Slide 22
Inconsistencies, discontinued model numbers can be exploited
Some bidders may normally include some GC work for common good
  Electrician including temporary power distribution even if not expressly required to do so by contract
Financial capacity and existing work volume must be verified
Proposal analysis can be qualitative, or subjective

## Slide 23
Some line items are okay for one contractor, but not for next
Unwillingness to compromise with language could mean the parties will not come to an agreement and go to contract
  Payment terms
  Scope items that were “snuck” into the contract
    Can cost you down the road if subs know this is typical of your firm
Be prepared for bargaining and negotiating the terms of each subcontract separately