## Slide 1: EE 620: Standards and Regulations of Communication Technology
Spectrum Management
    Made by
  Alwaleed A. Abdulwahed
    Supervisor
    Dr. Saud bin Saeed

## Slide 2
Agenda
1 | Introduction to Spectrum Management
2 | Spectrum Distributions in Saudi Arabia
3 | What is the benefits of Spectrum Management?
4 | Regional Distribution and Interference
5 | Why Operators Looking for More Spectrum?
6 | Spectrum Economic Value

## Slide 3
Introduction to Spectrum Management
Spectrum Management
The set of technical and administrative procedures.
To ensure the efficient performance of wireless services in a country.
To stop the interference (inside or over borders)
It is a global activity and decision.
Introduction to SM
Spectrum
It is referring to a range of radio-waves that are used for communication purposes
The Spectrum is a limited natural resource.
The spectrum starts practically from the 9 kHz frequency to the upper limit that extends to 3000 GHz.
Managing
Standardization

## Slide 4
Spectrum Distributions in Saudi Arabia
SM Assignment
Radio channel using spectrum management to manage the signal against interference
Also it is starting from 87.5 MHz to 108 MHz
The same thing in wireless but higher frequency
1800 MHz

## Slide 5
Spectrum Distributions in Saudi Arabia
20
20
SM Assignment
700 MHz
800 MHz
900 MHz
1800 MHz
2100 MHz
2300 MHz
2600 MHz
3500 MHz
3700 MHz

## Slide 6
Spectrum Distributions in Saudi Arabia
20
20
SM Assignment

## Slide 7
What is the benefits of Spectrum Management?
SM Benefits
We will reduce the interference between deferent countries by using agreed international approach
Reduce Interference
We can lower mobile equipment costs by standardization across technology providers
Reduce Cost
If we adopt an agreed international approach it will enable the roaming between countries
Mobility
Because the same products can be
sold internationally
Better Economies
SM
Benefits
ITU’s WRC: World Radio communication Conference, every three to four years set to discuss and agree changes to the ‘Radio Regulations’.
SM Benefits

## Slide 8
Regional Distribution and Interference
Region 1
Region 2
Region 3
Regional Distribution
ITU divides the world into three regions to have better SM
1 | Region 1 : Europe, Middle East, Africa, Russia and Mongolia
2 | Region 2 : The Americas including Greenland and some of the Eastern pacific Islands
3 | Region 3 : Asia pacific including most of Oceania
International SM

## Slide 9
Why Operators Looking for More Spectrum?
Data Growth
There are several important ways that mobile broadband networks
can support more data and achieve faster speeds:
We can improve the data and achieve faster speed by adding new layers
New Technology
We can improve the data and achieve faster speed by adding new sites
New Sites
We can improve the data and achieve faster speed by adding New frequency
New Spectrum
01
02
03
International SM

## Slide 10
Assigning Spectrum Internationally
Spectrum Auctions
The commanding method of assigning spectrum licenses to mobile operators is the spectrum auction
International SM

## Slide 11
National Spectrum Management
Spectrum Assignment Methods
There are a variety of approaches which regulators can use to exercise different levels of control over how spectrum is assigned
In this method the regulator has total control, including choosing which companies are assigned spectrum and how it used
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5
This method allows anybody to use a certain band without prior permission
This method uses market forces to determine the distribution of spectrum
Like Corona virus how it is pushing the governments to open new spectrums to have more capacity
The administrative approach
Market-based approach
The spectrum commons approach
National SM

## Slide 12
National Spectrum Management
Types of Licenses
Before issuing licenses, national governments first need to decide what kind of license to offer for each band
Which permits a specific type of equipment to transmit in a certain area at a specific frequency
A new approach that is
generally designed for bands
where there is a lower level of
demand
No license is required
in these bands
Individual License
Light License
License Exempt or Unlicensed
Licenses Types
National SM

## Slide 13
National Spectrum Management
License Terms
Regulators usually specify terms and conditions as part of a spectrum license which typically include:
Type of service that can be provided in a frequency band (e.g. only mobile services);
Technologies that may be used to transmit in the band (e.g. 2G, 3G, 4G or technology
neutral);
In the case of coverage bands (i.e. sub-1 GHz) there may be possible coverage obligations
(e.g. 90 per cent population coverage);
The duration of the license (e.g. 20 years).
National SM

## Slide 14
Spectrum Economic Value
The economic value of new spectrum
The main way regulators can quickly increase mobile network capacity by assigning spectrum licenses to mobile operators
Spectrum Economic Value

## Slide 15
Cellular Network Architecture
GSM Architecture
Cellular Network
UMTS Architecture
LTE Architecture

## Slide 16
Cellular Network Architecture
GSM Architecture
Cellular Network
Base Station Controller:
  Handling connections & Handover
  Radio Network Management
  Transcoding & Rate adapting
  Traffic concentration
  Transmission management of the BTS
  Remote control of the BTS
Base Transceiver Station:
  Antenna
  Transceiver (TRX)
  Power amplifier (PA)
  Combiner
  Multiplexer
  Alarm extension system
  Control function
  Baseband receiver unit (BBxx)

## Slide 17
TYPES OF BASE STATION
There are several types of base stations which support to serve the business need based on the consumer type
Propagation Environment
Outdoor
Macro cell
Indoor
Micro cell
DAS
Pico cell
Femto cell
Cellular Network
Cellular Network Base Station

## Slide 18
Cellular Network - SC
Cellular Network - Study Case
Sharing Site - Front View

## Slide 19
Cellular Network – Study Case
Sharing Site – Head View
Cellular Network - SC

## Slide 20
Cellular Network – Study Case
Sharing Site – Real example
Cellular Network - SC

## Slide 21: Stay safe, Stay
Home

## Slide 23
International spectrum management
International SM
Spectrum Legal Language
Allocate
A band is ‘allocated’ for potential use by a certain type of service (e.g. mobile, satellite or broadcasting) by a national regulator, which is contained in the National Frequency Allocation Table (NFAT), or on an international level through the ITU, as detailed in the ‘Radio Regulations’.
Identify
A band may then also be ‘identified’ for a limited range of technologies (e.g. a band that is ‘allocated’ to the mobile service will often be ‘identified’ for International Mobile Telecommunications (IMT) which means it can be used by a specific set of compatible mobile technologies, including all 3G and 4G systems).
Allot
A less-used term which refers to a decision made at a regional or national level to designate a frequency channel for use by a certain type of service in one or more countries
under certain conditions.
Assign
A specific frequency channel is then ‘assigned’ to a specific user by a national government or regulator (e.g. a band may be ‘allocated’ to the mobile service, ‘identified’ for IMT and then split into several sections which are each ‘assigned’ to different mobile operators).
Different words are used to describe whether a frequency band is available for use by a type of service, a limited range of technologies or a specific company.