# DCOM 217 W01 & W02: Cisco I – Introduction to Networks

# Midterm Skills Lab Exam – Spring 2021

This exam is open book (including electronic resources) and is to be completed by you only.

Assessment Due: Tuesday, April 27, 2021 11:59 PM

Honor Code: Students are not permitted to obtain information from or give information to other students during this exam. If such an attempt has occurred all students involved will obtain a grade of 0 (zero) for the exam. I have not obtained any help other than from my instructor. Student Signature: ______________________________ (Signature may be written or typed)

Submission Requirements:

- Create a new network using Packet Tracer.

- Submit the following as attachments to the Midterm Skills Lab in Blackboard:

  - This signed worksheet

  - The completed Packet Tracer file

Due Date/Time:

- April 27, 2021 11:59 PM

Total Points:

- 100 points

Assessments

Task 1: Create the Physical Topology

Task 2: Configure the Logical Topology

Task 3: Verify network connectivity

# Scenario

In this Skills Based Assessment students will create a small network that requires connecting network devices and configuring host computers, two switches, and one router for basic network connectivity. Common utility commands will be used to test the network.

# Topology Diagram

| Device Hardware Table |
| --- |
| Device | Qty | Description |
| Cisco Router | 1 | 4331 |
| Cisco Switch | 2 | 2960 |
| PC | 2 | Generic PCs |
| Cables | 4 | Copper straight-through |

Task 1: Create the Physical Topology (30 points).

Create a network using Packet Tracer

Open Packet Tracer and create a network according to the Topology Diagram and Device Hardware Table.

Ensure:

- The router cables are connected to the correct interfaces (ports).

- The PC FastEthernet0 interfaces are connected to FastEthernet interfaces on the switches.

- Note: Console interfaces are not used in this lab.

Task 2: Configure the Logical Topology

Step 1 - Configure IP Addressing according to the Device Addressing Table (2 points each).

| Device Addressing Table |
| --- |
| Device | Interface | IP Address | Subnet Mask | Gateway |
| Router | G0/0/0 | 192.168.5.1 | 255.255.255.0 | N/A |
|  | G0/0/1 | 10.20.30.1 | 255.255.255.0 | N/A |
| Switch1 | VLAN 1 | 192.168.5.2 | 255.255.255.0 | 192.168.5.1 |
| Switch2 | VLAN 1 | 10.20.30.2 | 255.255.255.0 | 10.20.30.1 |
| PC0 | Ethernet | 192.168.5.3 | 255.255.255.0 | 192.168.5.1 |
| PC1 | Ethernet | 10.20.30.3 | 255.255.255.0 | 10.20.30.1 |

Step 2: Configure the Router (3 points each).

| 1 | Router hostname | Router-Your-Name |
| --- | --- | --- |
| 2 | Console password | Cisco1 |
| 3 | Telnet (VTY) password | Cisco1 |
| 4 | Enable secret password | DCOM217 |
| 5 | Encrypt the clear text |  |
| 6 | Appropriate banner |  |
| 7 | Save the Running-Config file |  |

Note: Ensure the passwords are correct. If the passwords do not work for the instructor the student will receive a 0 (-21 points) for this part of the exam.

Router hostname – if your name is Prof Mayock, name the router: Router-Prof-Mayock

Step 3: Configure the two Switches (3 points each).

| 1 | Switch hostnames | S1 and S2 |
| --- | --- | --- |
| 2 | Appropriate banner |  |
| 3 | Save the Running-Config file |  |

Task 3: Verify network connectivity

Step 1: Use the ping command to verify network connectivity.

    - Verify connectivity with each network device.

  - Ping from one PC to all the IP Addresses.

If you are unable to ping the devices use Troubleshooting methods including:

- Show Run (sh run), Show IP Interface Brief (sh ip int b), ipconfig and other commands.

- Make sure the cables are connected to the correct interfaces (especially the routers).

- Check the IP Addressing on all devices.

- Check for IP Addressing activation (no shutdown) on the router and switch interfaces.

Save your Packet Tracer network and this document and submit both in Blackboard.