## Slide 1: HF Jet Ventilation vs HF Oscillatory Ventilation in Pediatric Care
Name of Author:
Institution:
Date:

## Slide 2: Objectives
Mechanism & Monitoring
Indications for HFJV & HFOV
Extubation for HFJV & HFOV
Notes: - Ventilation is a critical component of care in the pediatric and neonatal service delivery. Newborn babies with respiratory complications require adequate ventilation care to manage their conditions. The objective of the use of mechanical ventilation is to effectively support the exchange of gases with very minimal risk of ventilator-induced trauma on a patient (Meyers et al., 2019).
- These are the main areas of presentation in the HFJV & HFOV comparison

## Slide 3: HFJV…..
Uses a jet of gas to deliver high pressure gas at the rate of about 100 to 150 breaths per minute with less than four-tenth inspirational fraction (Ethawi et al., 2016).
A patient vital signs monitored; heartbeat, blood pressure, and the alveolar–arterial oxygenation difference etc.
The predetermined jet ventilator pressure limits should me monitored.
The CO2 monitoring is crucial even when the oxygen saturation is sufficient (Galmen et al., 2017)
To ensure accuracy, end-tidal CO 2 (ETCO2) is measured by periodic pausing (Galmen et al., 2017).
Notes: In HFJV, a catheter is inserted into a lumen of an endotracheal tube. A small cannula linked to a specialized ventilator transmits high pressure gas.
Unlike in HFOV, continuous monitoring of end-tidal CO2 (ETCO2) is not possible in a system exposed to the atmosphere, thus, period pausing allows for accurate measurement of end-tidal CO2 .

## Slide 4: HFOV…..
Uses electromagnetic diaphragm that supports respiratory rates of up to 900 breaths a minute via a conventional endotracheal tube (Carpi, 2017 .
Monitoring is needed regarding;
oxygenation index,
the heart rates,
blood pressure,
alveolar–arterial oxygenation difference,
arterial PH,
SpO2,
right ventricular load and transpulmonary pressure - (Meyers et al., 2019).
Notes: Klein (2020) asserts that the ability of the high frequency oscillatory ventilation to maintain ventilation and oxygenation while relying on minimal tidal volumes help reduce barotrauma and morbidity incases of newborns with respiratory distress syndrome.

## Slide 5: Indication- HFJV
Used in diagnostic laryngoscopy since the bore jet ventilation catheters are molded from floroplastic and non-flammable that offer greater advantage in laser surgery (Galmen et al., 2017).
In thoracic surgery such as in preterm infants due to minimal conflict of space (Galmen et al., 2017).
In chronic lung disease since it supports perfusion and allowing easy escape of CO2 (Maitra et al., 2015).
Effective among neonate with respiratory distress syndrome due to minimal constraints on the right regions of the heart (Galmen et al., 2017).
In effective during bronchopleural fistulae
In critical care due to lung protection (Galmen et al., 2017)
Notes: During thoracic surgery such as in preterm infants, the use of the narrow jet catheters since the easily pass through the surgical field thereby avoiding the conflict of space (Galmén et al., 2017).
In summary, HFJV in infant care best applies in diagnostic laryngoscopy thoracic surgery, chronic lung disease and in RDS

## Slide 6: Indication- HFOV
It is highly recommended for infant patients who not only have severe acute RDS but their lungs are unable to withstand high levels of tidal distending pressure (Carpi, 2017).
Notes: A great advantage with the use of the HFOV approach in such as case is that it offers a modality to enhance oxygenation and sustain peak airway pressure which would be equal to the mean airway pressure. The rationale is that though pressure wave at the endotracheal tube is slightly larger, the distending pressure onto the alveoli is almost equal to the mean airway pressure.

## Slide 7: Optimal Extubation
HFJV
- If PEEP or MAP is less or between 7cm and 8cm H20 with FiO2 ≤ 0.35 and Jet PIP (less than 20 with a delta p less than 10) (Klein, 2020).
HFOV
- Among infants born with extremely low birth weight (ELBW), it was found that feasible levels are at MAP ≤6 cm H2O with FiO2 ≤0.25 (Tana et al., 2018).
Extubation for HF is ideal when the peak aspiratory pressure is around 8 cm H2O with FiO2 less than 0.30 (Sant’Anna and Keszler, 2012).
Notes: -For HFJV, if the sopharyngeal continuous positive airway pressure (NPCPAP) is between 6cm -8cm H2O), it is permitted to undertake extubation for the patient.
- For the HFOV, the ideal level would be MAP ≤6 cm H2O with FiO2 ≤0.25 (Tana et al., 2018). Levels below this value would result in extubation failure and immediate need for re-intubation (Szymankiewicz et al. 2005).

## Slide 8: References
Carpi, M. (2017). High-Frequency Jet Ventilation in Preterm Infants: Is There Still Room for It? Respiratory Care, 62 (7) 997-998; DOI: 10.4187/respcare.05647
Galmén, K., Harbut, P., Freedman, J., & Jakobsson, J. G. (2017). The use of high-frequency ventilation during general anesthesia: An update. F1000Research, 6, 756. https://doi.org/10.12688/f1000research.10823.
Gupta P, Green JW, Tang X, et al. (2014). Comparison of High-Frequency Oscillatory Ventilation and Conventional Mechanical Ventilation in Pediatric Respiratory Failure. JAMA Pediatr, 168 (3):243–249. doi:10.1001/jamapediatrics.2013.4463
Klein, J. (2018). Management strategies with high frequency jet ventilation in neonates. University of Iowa Stead Family Children’s Hospital. Retrieved on 29 November 2020 from https://uichildrens.org/health-library/management-strategies-high-frequency-jet-ventilation-neonates
Maitra S, Bhattacharjee S., & Khanna P., et al. (2015). High-frequency ventilation does not provide mortality benefit in comparison with conventional lung-protective ventilation in acute respiratory distress syndrome: A Meta-analysis of the randomized controlled trials. Anesthesiology, 122(4):841–51. 10.1097/ALN.000000000000030
Meyers, M., Rodrigues, N., & Ari, A. (2019). High-frequency oscillatory ventilation: A narrative review. Canadian journal of respiratory therapy, 55, 40–46. https://doi.org/10.29390/cjrt-2019-004
Sant’Anna, D., and Keszler, M. (2012). Weaning Infants from Mechanical Ventilation. Clin Perinatol, 39, 543–562 Doi: 10.1016/j.clp.2012.06.003
Szymankiewicz, M., Vidyasagar, D., & Gadzinowski, J. (2005). Predictors of successful extubation of preterm low-birth-weight infants with respiratory distress syndrome. Pediatr Crit Care Med, 6 (1), 44-50 DOI: 10.1097/01.PCC.0000149136.28598.14
Tana, M., Lio, A., Tirone C & Aurilia, C et al. (2018). Extubation from high-frequency oscillatory ventilation in extremely low birth weight infants: a prospective observational study. BMJ Pediatrics Open, 2:e000350, 1-7 Doi: 10.1136/bmjpo-2018-000350