## Slide 1: IENG 461 – System Safety I Lecture 6 – Preliminary Hazard Analysis (PHA)
James R. Harris, Ph.D., P.E.

## Slide 2: Preliminary Hazard Analysis
Overview of tonight’s topics
  Background/history
  PHA execution
  Practical examples
  Homework #3 assignment
  Project discussion
  Exam 1 review

## Slide 3: Preliminary Hazard Analysis
Background
MIL-STD 882 – beginning of system safety
  PHA is first analysis task
Very preliminary tool – used early in design cycle
Brainstorming concept
More detailed analysis to follow…

## Slide 4: Preliminary Hazard Analysis
PHA execution
Hazard list
  Mechanical, electrical, chemical, radiation, thermal, (biological)
Determine
  Cause
  Consequence
  Initial risk (optional)
  Risk reduction measures
  Residual risk (optional)

## Slide 5: Preliminary Hazard Analysis
Expansion on basic hazard categories:
Mechanical:
  Crushing surfaces
  Ejected parts/fragments
  Rotating equipment (in-running nip points)
  Sharp edges
  Stability

## Slide 6: Preliminary Hazard Analysis
Electrical:
  Arcing
  Electromagnetic interference
  Ignition of combustibles
  Power outage
  Shock

## Slide 7: Preliminary Hazard Analysis
Chemical
  Corrosion
  Exposure to aerosol
Radiation
  Ionizing
  Nonionizing

## Slide 8: Preliminary Hazard Analysis
Thermal
  Burns
  Elevated flammability
  Elevated gas/liquid pressure
  Elevated reactivity
  Elevated volatility

## Slide 9: Preliminary Hazard Analysis
Sources of information:
  Past incident reports
  Expert opinion (can include many disciplines…not just engineers!)
  External opinion (fresh eyes from outside the company) --- (show checklist)

## Slide 10: Preliminary Hazard Analysis Example: PRT
Hazard (Mechanical) | Cause | Consequence | Risk reduction | Assigned to:
Pedestrian struck by car | Pedestrian on track | Death | (Eliminate) Prevent unauthorized track access (Eng Control) Detect objects on track and prevent car motion | Team 1
Rider struck by closing door | Rider unaware door is closing | Minor injury? | (Admin Control) Announce door closing | Team 2
Note that risk has not been estimated.

## Slide 11: Preliminary Hazard Analysis Example: Coffee maker
Hazard | Cause | Consequence | Risk reduction | Assigned to:

## Slide 12: Preliminary Hazard Analysis
Summary
PHA comes early in the designing phase – not many details needed
Team approach is important
Work through the general categories of hazards

## Slide 13: Preliminary Hazard Analysis
Preview of next week
  NO CLASS NEXT WEEK…Fault Tree Analysis and Failure Modes and Effects Analysis the next week
Homework 3: Part 1: Pick 4 products or systems you are familiar with and perform a PHA for each product. Consider hazards from all of the general categories (mechanical, electrical…) we have discussed. In the risk reduction column, make suggestions from two levels of hazard control hierarchy. Part 2: Turn in one paragraph describing the product or process you will use for your class project. Due by email (filename lastname_HW3) before 5:30pm, Oct. 17
Questions?