## Slide 1: IENG 461 – System Safety I Lecture 7 – Fault Tree Analysis (FTA)
James R. Harris, Ph.D., P.E.

## Slide 2: Fault Tree Analysis
Overview of tonight’s topics
  Introduction
  FTA execution
    Qualitative
    Quantitative
  Practical examples

## Slide 3: Fault Tree Analysis
Introduction
Initiated at Bell Labs for Air Force – 1962
Deductive technique
  Starts with general and moves toward specific
  Requires knowing the “top event” or end point in advance
  More detailed design information needed compared to PHA

## Slide 4: Fault Tree Analysis
Methodology…
General rules:
  Moving down the tree reveals causes
  Moving up the tree reveals effects
  No gate to gate connections
  Do not draw lines from two gates to single input
  Bottom level of tree should not be rectangles (For example, need basic event or undeveloped event)

## Slide 5: Fault Tree Analysis
AND gate – all inputs to gate required
OR gate – any input to gate is sufficient
Basic event
Event

## Slide 6: Fault Tree Analysis
Connecting symbol (can be used to jump to another fault tree)
Undeveloped event

## Slide 7
Amputate finger with table saw
Finger contacts blade
Blade is rotating
No guard in place
Finger around guard
Saw plugged in
E-stop not pushed
Switch toggled on
Ask: What could cause this?
Level 1
Level 2

## Slide 8: Fault Tree Analysis
Group exercise 1

## Slide 9: Fault Tree Analysis
Quantitative analysis rules:
  Boolean algebra is used
  Label each event
  B1.B2 = AND
  B1+B2 = OR

## Slide 10: Fault Tree Analysis
Boolean algebra simplification
  a.a=a
  a+a=a
  a+a.b=a
  a.(a+b)=a
  a.(b+c)=a.b+a.c
  a.b+a.b.c=a.b

## Slide 11
T
B
C
B
D
Group Exercise #2

## Slide 12: Fault Tree Analysis
Cut sets – group of events that, if they all occur, would cause the top event
Minimal cut set – the cut set with the fewest events which could lead to the top event
Single-point failure – single occurrence that leads to incident

## Slide 13: Fault Tree Analysis
Group exercise 3

## Slide 14: Fault Tree Analysis
Summary
FTA useful to identify basic events (root causes)
Identifying cut sets and minimal cut sets is important
One disadvantage: You need to know top events in advance