## Slide 1: MECHANICAL VENTILATORS
HOW MECHANICAL VENTILATORS OPERATE

## Slide 2: Settings in the initial mechanical ventilator
Mode : Assist Control mode
Tidal volume is set depending on lung status :Normal = 12 mL/kg ideal body weight; COPD = 10 mL/kg ideal body weight; ARDS = 6-8 mL/kg ideal body weight.
Oxygen Concentration: at first select high (100%) FI02 and adjust when obtaining ABGs after 20 min.
Set rate: the initial set rate should be close to the patient’s total rate and slowly decrease it with the patient’s tolerance.
Notes: COPD refers to Chronic Obstructive Pulmonary Disease
ARDS is Acute Respiratory Distress Syndrome
PEEP= Positive End-Expiratory Pressure it is used together with mechanical ventilation to maintain the patients airway pressure above the atmospheric level.
Peep may be required to achieve a decrease in FI02.

## Slide 3: Settings continued
Inspiratory flow rate: For optimal gas exchange use IFR of 60L Per minute; for patients with COPD use 100L/min .
Peep: only as indicated after first arterial gas determination; not greater than 25%
Inspiration expiration ratio : usually 1:2; foe inverse ratio ventilation up to 4:1

## Slide 4: Volume V pressure control ventilation
In VCV, theirs is preset tidal volume and minute ventilation but the clinician is required to set the appropriate inspiratory flow, flow waver form and the inspiratory time.
PCV limits the maximum air pressure but this could lead to variable tidal and minute volume.
In PCV, the clinician is required to titrate the inspiratory pressure to the measured tidal volume.

## Slide 5: Improving oxygenation in a ventilator
To improve oxygenation:
Increase FI02
Increase the mean alveolar pressure ;Increase mean airway pressure ;Increase PEEP; increase I:E ratio
Re-open alveoli with peep

## Slide 6: Improving ventilation in a ventilator
Modify alveolar ventilation by raising the rate or tidal volume and increasing T low increases ventilation while reducing C02.

## Slide 7: ARDS Patients
To improve mortality for patients who develop ARDS, an open lung strategy with high PEEP and low tidal volume is recommended.
Notes: ARDS is a type of non-cardiogenic pulmonary edema.

## Slide 8: REFERENCES
Wilcox, S. R., Richards, J. B., Fisher, D. F., Sankoff, J., & Seigel, T. A. (2016). Initial mechanical ventilator settings and lung protective ventilation in the ED. The American journal of emergency medicine, 34(8), 1446-1451.
Vieillard-Baron, A., Matthay, M., Teboul, J. L., Bein, T., Schultz, M., Magder, S., & Marini, J. J. (2016). Experts’ opinion on management of hemodynamics in ARDS patients: focus on the effects of mechanical ventilation. Intensive care medicine, 42(5), 739-749.
Rittayamai, N., Katsios, C. M., Beloncle, F., Friedrich, J. O., Mancebo, J., & Brochard, L. (2015). Pressure-controlled vs volume-controlled ventilation in acute respiratory failure: a physiology-based narrative and systematic review. Chest, 148(2), 340-355.