## Slide 1: Regulation of Good Food Production Practices AS.410.686.81.FA21
MODULE 2: GMPs & GAPs/GHPs
Kantha Shelke, Ph.D.
KShelke1@jhu.edu
kantha@corvusblue.net
(o) 312-951-5810 | (c) 312-437-5810

## Slide 2: Learning objectives
Understand the basic requirements of Good Manufacturing Practices (GMPs) for human food
Understand the fundamentals of Good Agricultural Practices / Good Handling Practices
Learn the definition of prerequisite programs and their importance in a food safety program
Learn where to find more information on GMPs and GAPs

## Slide 3: GMPs
Good Manufacturing Practices

## Slide 4: What are GMPs?
The Good Manufacturing Practices (GMPs) are regulations that describe the methods, equipment, facilities, and controls required for producing human and veterinary products, medical devices, and processed food.
The U.S. regulations are called "current" Good Manufacturing Practices (cGMPs), to emphasize the dynamic expectations.
Current food good manufacturing practices (GMPs) are published in Title 21 of the Code of Federal Regulations, Part 110 (21 CFR 110).
As the minimum sanitary and processing requirements for producing safe and wholesome food, GMPs are an important part of regulatory control over the safety of the nation's food supply.
GMPs serve as a basis for FDA inspections.
The GMP regulations address requirements for many prerequisite programs. There are other programs that are likely to apply to most facilities, such as supplier and manufacturing specifications.
GMPs ARE NOT OPTIONAL!

## Slide 5: Why GMPs exist
Good Manufacturing Practices define a quality system that manufacturers use to build quality INTO their products.
The ultimate objectives for developing and producing food products according to GMPs are to ensure “safety and properly processed and packaged products of high quality”.
Definitions:
Prerequisite program: Procedures, including Good Manufacturing Practices (GMPs) that provide the basic environmental and operating conditions necessary to support the Food Safety Plan.
Food safety system: The outcome of implementing the Food Safety Plan and its supporting elements.

## Slide 6: Prerequisite programs
Prerequisite programs provide the basic environmental and operating conditions that are necessary to support the Food Safety Plan.
In some cases these programs are part of the Food Safety Plan.
Many of these programs are required by regulation (e.g., GMPs).
The specific prerequisite programs required may vary depending on the type of food produced and the facility where it is processed or held.
The terms prerequisite program, GMP, cGMP (“c” stands for current), “good hygienic practice” and “sanitation standard operating procedures” are often used interchangeably.
The important thing to remember is that these are foundational programs included in an overall food safety system.
Without these programs, the Food Safety Plan may not successfully prevent food safety issues.
Remember that the Food Safety Plan focuses on what matters most to ensure the safety of the food being produced.

## Slide 7: How GMPs were developed
The GMP regulations were finalized in April, 1969, published as 21 CFR 128, then recodified and published as 21 CFR 110 in 1977.
The published GMP regulations were broad and did not specify what exactly a facility must do to comply. The ambiguity created enforcement problems for the FDA and the FDA tried to develop industry-specific GMPs.
In the late 1970s, FDA began to revise the umbrella GMPs instead of adopting industry-specific GMPs. These revisions were finalized and published in 1986 in 21 CFR 110.
Specific GMPs were also published in 21 CFR Parts 100—169 for:
  Quality control procedures for nutrient content of infant formula (21 CFR 106).
  Thermally processed low-acid canned foods in hermetically sealed containers (21 CFR 113).
  Acidified foods (21 CFR 114).
  Bottled drinking water (21 CFR 129).
  Fish & Fishery Products (21 CFR, Part 123).

## Slide 8: A timeline of GMPs
The original GMPs regulation was very broad and did not really serve any industry as such.
FDA attempted to develop specific industry GMPs and concluded it was more effective to strengthen “umbrella” GMPs and established a cGMP regulation in 21 CFR Part 117.
FDA has additional cGMPs for certain types of foods:
Dietary Supplements - 21 CFR Part 111. See https://bit.ly/2uTGFdc
Infant Formula - 21 CFR Part 106: https://bit.ly/2uQbbVu
Low-acid Canned Foods - 21 CFR Part 113 https://bit.ly/2UW0pYo
Acidified Foods - 21 CFR Part 114 https://bit.ly/37zbQrN
Bottled Water - 21 CFR Part 129
  https://bit.ly/2SNYiTT

## Slide 9: How GMPs change
GMPs change formally and informally.
Expect significant changes with advances in food processing and food distribution technologies.
Example of a formal change:
In September 2015, when FDA created rules for the FSMA, it also updated GMPs. FDA made a formal change in the cGMPs to include provisions intended to reduce the number of allergen recalls based on the growing number of people with food allergies and undeclared allergens becoming the top reason for food recalls.
General provisions of the GMPs provide definitions which are important in understanding implications and applications. Management has responsibility for performance of personnel under GMPs.

## Slide 10: GMPs in different countries
At a high level, GMPs of various nations are very similar.
Most require:
  Equipment and facilities are properly designed, maintained, and cleaned
  Standard Operating Procedures (SOPs) be written and approved
  An independent Quality unit (like Quality Control and/or Quality Assurance) to be well trained personnel and management

## Slide 11: GMPs in general
Determines whether the facilities, methods, practices and controls used to process food are safe and whether the food has been processed under sanitary conditions
Determines whether food is adulterated under the FDCA.
All employees of enterprises that manufacture, process, pack or hold food must be trained in principles of food hygiene and food safety, including in importance of employee health & hygiene.
Not "process specific" but related to the entire operation.
GMPs include facilities/grounds, equipment pest control, receiving and storage, process control, product recall and personnel training.
Product-specific GMPs include:
  Thermally processed low-acid canned foods
  Acidified foods
  Bottled drinking water
  Infant formula
  Fish and fishery products

## Slide 12: Components of GMPs
Regulation 21 CFR 117 Subpart B lists the following components that establish the conditions and practices the food industry must follow for processing safe food under sanitary conditions:
Personnel
Plants and grounds
Sanitary operations*
Sanitary facilities and controls
Equipment and utensils
Processes and controls*
Warehousing and distribution
Holding and distribution of human food by-products for use as animal food
Defect action levels
*Some components may be preventive controls based on hazard analysis. Some elements controlled by GMPs in the past have been called by FDA and reviewed / updated

## Slide 13: Training
Individuals must be qualified by education, training, or experience to manufacture, process, pack, or hold food.
Individuals must receive food hygiene and food safety training.
Supervisors responsible for ensuring compliance must have appropriate knowledge, training, or experience.
Employee education and training is an important prerequisite program. Employee training must cover cleanliness, health requirements, how to perform their job and how their work can impact the safety of product. This employee training must be documented. Supervision and setting a good example is also an important part of the system.

## Slide 14: Personnel
Restricting persons with illness or open wounds
Proper handwashing and sanitizing
Adequate personal cleanliness
Suitable gloves maintained in satisfactory condition
Suitable outer garments
Jewelry removed
Hair restraint
Personal items stored away from production areas
No eating, drinking or tobacco use in production area
Food handlers with vomiting, diarrhea, jaundice, sore throat with fever, wounds or open lesions could be a source of microbiological contamination that could lead to foodborne illness.
Procedures and practices must make sure that sick people are not around food, and employees must receive training on this.

## Slide 15: Important definitions
Direct contamination – transfer of human pathogens, e.g. after using the restroom or after sneezing.
Cross‐contamination – Unintentional transfer of a pathogen from a food or surface to another food or surface.
Allergen cross‐contact – Unintentional incorporation of a food allergen into a food.
People are also a potential source of contaminants entering the processing environment. Therefore, clothing must be clean. Dedicated footwear, color coding, and other relevant clothing options should be considered depending upon the needs of the operation.
Proper hand washing (and hand sanitizing when handling ready‐to-eat foods) is essential (each time employees are away from the workstation) to prevent direct contamination, cross-contamination, and allergen cross‐contact.

## Slide 16: GMPs: Plants and grounds (1/2)
Removal of debris, unused equipment and uncut vegetation
Proper drainage of grounds
Proper waste disposal
Adequate space for operations and for cleaning
Proper separations of operations to prevent cross-contamination and allergen cross contact
Cleanable walls, floors and ceilings and all kept in good repair
Prevent drip or condensate from contaminating the product at any part of the operation
Adequate lighting
Guard against glass breakage; generally, no glass is allowed inside manufacturing
Adequate ventilation that does not contaminate the product and negative air pressure in production facilities
Screened openings to the outside

## Slide 17: GMPs: Plants and grounds (2/2)
Buildings must be designed and constructed to facilitate effective maintenance and sanitation
Results specified rather than method for achieving
Detailed expectations in sanitation of operations
GMPs listed above for the plant and grounds help to ensure that the buildings and structures are suitable for food‐production purposes, and to reduce the potential for pathogen recontamination. For example, make sure that the grounds outside the food facility are clean, that there is no standing water, and that waste is collected and disposed of frequently. Inside the facility provide adequate space and proper separation for operations (e.g., between cooked and raw product and between food with different allergen profiles, if applicable). Also, make sure that walls, floors and ceilings are in good repair. It is also important to ensure that condensate does not drip onto in‐process product, that there is adequate light for operations, and that any glass is guarded against breakage

## Slide 18: GMPs: Equipment and utensils
Equipment, including utensils, must be designed to be adequately cleaned and maintained in a sanitary condition.
Food-contact surfaces must be corrosion resistant and non-toxic to preclude adulteration of any kind.
Compressed gases introduced into food must be treated so that it does not contain adulterants and be properly filtered to prevent particles from getting into food.
Freezers and coolers have temperature indicating devices and automatic temperature control and alarm systems.
Properly maintain accurate process control instruments. Thermometers and similar equipment must be accurate (close to the correct measure), precise (appropriately narrow range) and maintained.
Automatic temperature control or an alarm system helps to ensure that the proper temperatures are maintained.

## Slide 19: GMPs: Production and process controls
Processes and controls used for food must ensure that the food remains suitable for human consumption. This provision covers general and more specific requirements for raw materials, ingredients, and manufacturing operations.
The GMPs emphasize end results ensuring that no adulterated food enters marketplace. Terms used, however, are subject to variation in interpretation. This is the main reason why competent individuals are an imperative for food production facility. Personnel should be trained and aware of GMP requirements. They MUST know how, why, and what to do.
Raw materials and ingredients properly inspected, analyzed, segregated, stored, and handled appropriately.
Manufacturing operations must be monitored in terms of pH, water activity, temperatures for various steps, and guarding product from metal.

## Slide 20: GMPs: Raw materials and ingredients
Comply with FDA requirements for pests, extraneous materials (e.g., string, plastic, metal, etc.), and undesirable microorganisms, as assured by testing, supplier certification (Certificates of Analysis), or heat treatment. Plants are responsible for assuring this using whatever techniques are appropriate for the material and your source of supply.
Raw materials must be inspected for suitability.
Raw materials must be stored and handled to prevent contamination (e.g., properly packaged) and deterioration (e.g., appropriate time, temperature and humidity conditions). This also applies to thawing.
If rework is used, rework must be identified properly, stored and handled to prevent contamination, allergen cross‐contact and deterioration.

## Slide 21: GMPs: Manufacturing operations (1/3)
Prevent microbial growth through:
  Cooking
  Time/temperature control
  Water activity control
  pH control
Use clean and sanitized equipment, utensils, and finished product containers.
Manufacture ice from potable water in a sanitary manner.
Prevent cross-contamination and allergen cross-contact.
All manufacturing operations must be conducted to minimize microbial growth. Pasteurizing, freezing and refrigerating are food processing methods that may be used to prevent spoilage and ensure safety of certain food products. The extent to which these are used depends on the particular product and its distribution.

## Slide 22: GMPs: Manufacturing operations (2/3)
When used, these processes must be done in a manner that ensures the conditions are adequate to maintain product safety and prevent deterioration, including use of time and temperature combinations that kill pathogens of concern (for pasteurization) and that prevent the growth of microorganisms during cooling in refrigeration and freezing processes.
Rapid cooling or further processing without delay of blanched foods is necessary to prevent microbial growth. Certain bacteria, called thermophiles (thermo=heat, phile= loving), can grow at hot temperatures. Minimize thermophilic growth through proper temperature and timely cleaning.
Certain moist foods such as batters, breading, sauces, gravies, and stuffing can support rapid growth of microorganisms. Protect these from contamination through good quality ingredients, heat treatment, time/temperature controls, and physical protection such as covers.
Dry foods that depend on low water activity to control microbial growth must have parameters (e.g., soluble solids/water ratio or water activity) monitored to assure that growth is controlled and protected from moisture pickup.

## Slide 23: GMPs: Manufacturing operations (3/3)
Equipment, utensils and finished product containers must be cleaned and sanitized as necessary to ensure sanitary conditions. This may require disassembly of equipment to facilitate cleaning.
Ice is a common ingredient for many operations. If made in‐house, it must be made from potable water and produced in a sanitary manner. Ice machines, like other food processing equipment, must be cleaned and sanitized periodically.
Finished or in‐process food must be protected from contamination by raw materials or refuse. This includes exposed food on conveyors in the ambient environment, as well as in freezers and coolers.
Use of sieves, traps, magnets and metal detectors can be useful to prevent inclusion of metal and extraneous material, or to detect metal if such contamination does occur.
Destruction and reconditioning operations should not serve as sources of contamination and methods used should be shown to be effective.

## Slide 24: GMPs: Warehousing and distribution
Sanitary conditions apply not only to manufacturing areas, but also to warehousing and distribution.
Microbial growth must be prevented.
Allergen cross‐contact must be prevented.
GMPs require that food is protected from biological, chemical (including radiological) and physical hazards, as well as from deterioration during warehousing and distribution.

## Slide 25: GMPs By-products sent to animal food
Food companies often send unusable food (unsalable to humans for quality or safety reasons but could be safe or made safe for animals) or by‐product materials to the animal food supply chain.
By‐products might be sent to animal feed converters, manufacturers or wholesalers; or directly to animal producers that may feed it directly to animals or, if necessary, process the food to mitigate any hazards.
Human food and by‐products held and sent to the animal food supply chain in general are not subject to the requirements for hazard analysis and risk‐based preventive controls for animals but must comply with specific holding and distribution GMPs to keep the byproduct safe (21 CFR 117.95 and 21 CFR 507.28). For example,
  Ensure the safety of containers
  Avoid contamination from trash or garbage
  Identify the material during labeling
Note: If a human food manufacturer also processes by‐products by drying, pelleting, grinding, it must comply with the Preventive Controls for Animal Food regulation in 21 CFR Part 507.

## Slide 26: GMPs: Defect Action Levels
Definition of defect action level (DAL): A level of a non‐hazardous, naturally occurring, unavoidable defect at which FDA may regard a food product “adulterated” and subject to enforcement action under section 402(a)(3) of the FDCA. (Source: 21 CFR 117.3)
Even when produced under GMPs, some foods may contain natural or unavoidable defects that are not harmful at levels present.
FDA establishes DALs when necessary and possible and will use these levels when deciding whether to recommend regulatory action. The manufacturer is still responsible for managing these defects, and trying to keep them to the lowest level currently feasible. For example, a few pit fragments in pitted dates, olives and prunes may be considered unavoidable even under GMPs.
Defect level may not be reduced by blending. Mixing of food containing defects above the defect action level with another lot of food with low levels is not permitted –the entire batch would be considered adulterated regardless of the level present.

## Slide 27: Summary of general GMPs
Intended to prevent adulteration
Opportunity for considerable judgment in defining and interpreting regulations
The “spirit” of GMPs is to do what is reasonable and necessary to ensure safe and unadulterated food supply

## Slide 28: Product-specific GMPs: Low acid canned food
Life threatening risk if improperly processed
Requires supervision of personnel who have been trained
Regulations quite detailed for equipment design and operation
Extensive record keeping requirements

## Slide 29: Product-specific GMPs: Acidified foods
Defined as a low acid food with
  Aw greater than 0.85
  acid added to lower pH to 4.6 or lower
Product examples
  includes beans, cucumbers, cabbage
  excludes carbonated beverages
Personnel trained under approved program

## Slide 30: GMPs: Bottled drinking water
All water sealed in bottles, packages for human consumption
Regulations are general and similar to umbrella GMPs
Source of water must be approved
Sanitation, equipment designed, personnel emphasized
Extensive record keeping

## Slide 31: GMPs: Dietary Supplements
Under the Dietary Supplement Health Education Act (DSHEA) of 1994, the manufacturer is responsible for ensuring that the dietary supplement is safe before it is marketed.
FDA can take action if the dietary supplement product is adulterated or misbranded.
Dietary supplement manufacturers follow the general food GMPs.

## Slide 32: Prerequisite programs
Prerequisite programs deal with the “good housekeeping” concerns of the establishment and consist of steps or procedures, including GMPs and SSOPs, that are taken to control the operational conditions within a food establishment and which promote environmental conditions that are favorable for the production of safe food.
Prerequisite programs are the foundation of a Food Safety/HACCP system.
Hygienic zoning is an important prerequisite program in ready-to-eat facilities.
Supplier and product specifications.
In practice, a preventive maintenance schedule includes steps such as cleaning and facility maintenance which when regularly scheduled can greatly minimize food safety issues.
Signage or color coded equipment and utensils.
Others, specific to the plant or the product.

## Slide 33: Prerequisite program: Hygienic zoning
Hygienic zoning is useful to reduce the potential spread of pathogens in facilities that manufacture ready‐to‐eat (RTE) products. For example, areas of the facility that handle the raw ingredient (e.g., raw peanuts) may have less stringent expectations for hygiene than those handling the RTE product (e.g., roasted peanuts).
Zoning typically involves separation of, for example, cooked product from raw product, and may include different uniforms for “cooked side” and “raw side” employees, dedicated equipment (e.g., carts or fork lifts) for different zones, traffic flow and air flow considerations, etc.
Some elements of hygienic zoning may be a preventive control as determined through the hazard analysis process.

## Slide 34: Prerequisite program: Purchasing and manufacturing specifications (1/2)
Written specifications for the products produced and the processes used to make them, as well as ingredient and packaging materials, are common in business transactions.
Well written specifications help to ensure that expectations are understood by both the customer (the manufacturer in this case) and the supplier.
This is particularly important for ingredients that have a history of association with foodborne hazards.
Efforts should be made to know suppliers, such as learning about their facilities and practices, and the safety and quality of their products.
Buying ingredients on the open market and spot markets such as Internet portals without knowledge of the supplier’s food safety practices or program can add risk to food operations.
Written ingredient and packaging material specifications should be developed for all suppliers, and verification of compliance with those specifications is recommended for ingredient classes that have a history of contamination.

## Slide 35: Prerequisite program: Purchasing and manufacturing specifications (2/2)
Adherence to the specification is commonly confirmed through the use of a letter of continuing guarantee or a certificate of analysis (COA) that verifies the ingredient or product meets specifications.
Some ingredients have a history of outbreaks associated with specific foodborne hazards and plant operators must be familiar with every ingredient procured for their manufacturing operation.
Periodic reviews of the supplier’s product against ingredient specification requirements should be an element of supply‐chain programs.
Use of a third‐party auditing firm that reviews the supplier’s food safety program is one way to verify that controls are in place at the supplier.
The extent to which controls are used should be risk‐based and consistent with regulatory requirements.

## Slide 36: Operation-specific prerequisite programs
Some manufacturing enterprises develop detailed procedures that may also be considered prerequisite programs.
These may include receiving, storage and shipping procedures, labeling and label review, ingredient handling practices, glass control, visitor control, etc.
The impact of these programs on food safety can be considered during the hazard analysis process.
For example, labeling foods that contain food allergens is a preventive control that must be included in the Food Safety Plan, but label review for other information may be a prerequisite program.
Similarly, glass control programs may be a prerequisite program for facilities that do not pack in glass containers; however, preventive controls would be required if glass containers are used in a facility.

## Slide 37: GMPs and prerequisite programs
GMPs and other prerequisite programs provide the foundation necessary for production of safe and wholesome food.
Good Manufacturing Practices and other prerequisite programs must be in place to provide a solid foundation for the Food Safety Plan. In fact, GMPs are required by regulations and most are managed as prerequisite programs outside the Food Safety Plan.
GMPs are operationalized by workers, frequently through written SOPs (Standard Operating Procedures).
This module is designed only to provide a brief overview of GMPs.
Because all GMPs are required, additional training or in‐depth reading of the GMP regulations is important to ensure that the specific requirements are addressed. Training is important to understand and effectively implement GMPs.

## Slide 38: Relevant reading
The World Is Changing and So Must Your Food Safety Expectations https://goo.gl/rE7wEz
Ensuring the Safety of Food Contact Materials: GMPs and Beyond https://goo.gl/anGV1F
FDA’s top 5 most commonly cited food safety violations https://goo.gl/Quzmvz

## Slide 39: GAPs/GHPs
Good Agricultural Practices (GAPs) and Good Handling Practices (GHPs) are voluntary audits that verify that fruits and vegetables are produced, packed, handled, and stored as safely as possible to minimize risks of microbial food safety hazards.
USDA GAP & GHP audits verify adherence to the recommendations in FDA’s Guide to Minimize Microbial Food Safety Hazards for Fresh Fruits and Vegetables and industry-recognized food safety practices.

## Slide 40: Good Agricultural Practices (GAPs)
Definition of Good Agricultural Practices (GAPs): A collection of principles to apply for on-farm production (pre-planting, planting, harvest) and post-harvest (sorting, packing and storage operations), resulting in safe and healthy food and non-food agricultural products, while taking into account economical, social and environmental sustainability.
These practices may be applied to a wide range of farming system and at different scales. They are applied through sustainable agricultural methods, such as
  Integrated pest management
  Integrated fertilizer management
  Conservation agriculture.
GAPs rely on four principles:
  Economically and efficiently produce sufficient (food security), safe (food safety) and nutritious food (food quality);
  Sustain and enhance natural resources;
  Maintain viable farming enterprises and contribute to sustainable livelihoods;
  Meet cultural and social demands of society.

## Slide 41: Food safety for produce: GAP background
People in the USA have been increasing their consumption of fresh fruits and vegetables since 1970
Fruits and vegetables are available year-round, and therefore:
  being shipped longer distances, and
  during off-season may be coming from outside US
Generally grown in an open environment
Multiple opportunities for contamination
No absolute kill step without damaging quality
Situations of disease outbreaks have been traced to fresh produce contamination
Food borne illness outbreaks associated with growing and handling practices
Resulting in methods aimed at reducing contamination: HACCP- Hazard Analysis and Critical Control Point (meats, poultry & eggs, seafood)

## Slide 42: Food safety for produce: GAP/GHP background
In 1998 the FDA published the Guide to Minimize Microbial Food Safety Hazards for Fresh Fruits and Vegetables
This was the beginning of GAPs in the commercial food production sector.
Efforts are now underway in the US and in Europe - (EuroGAP)
GAPs are now being adopted and enforced around the world, either through various national regulatory agencies or by the importers as part of the Foreign Supplier Verification Program.
Definition of Good Handling Practices (GHP) are voluntary audits that verify that fruits and vegetables are packed, handled, and stored as safely as possible to minimize risks of microbial food safety hazards

## Slide 43: GAP goals
Goal is to produce safe, wholesome fruits and vegetables
Production and post-harvest voluntary evaluation to reduce the risk of human disease contamination on fresh produce
A comprehensive examination of the growing and harvesting operations and of the post-harvest handling
Examination goal is to identify potential areas of contamination
Water quality and use
Land use
Worker health, hygiene and training
Manure and compost
Wildlife and animal management
Sanitation and postharvest handling
Transportation
Traceability

## Slide 44: Water quality and use
Water quality must be appropriate for:
  Crop
  Type of irrigation method and/or application
Test water quality
Water use:
  Application spray or fertilizers
  Irrigation method
  Harvest
  Wash produce

## Slide 45: Land use
Past
Current
Nearby– animal operation or grazing
History of flooding

## Slide 46: Worker health, hygiene and training
The need for training has never been more critical than it is today.
The rationale for this is that FDA has identified an association between foodborne illness and lack of understanding of GMP fundamentals. The agency estimates that up to one-third of all GMP-related recalls are the result of inadequate training and education.
Consequently, it is vital that employees receive documented training and education in food safety principles and cGMPs. Train employees:
  How to properly wash hands
  How to handle & report injuries & illnesses
Provide clean, accessible, well-stocked restroom facilities and handwashing stations
Designated areas for eating and smoking

## Slide 47: Manure and compost
Raw manure application intervals based on USDA National Organic Program:
  2 weeks prior to planting
  120 days prior to harvest
Composting is a managed process, grower must monitor:
  turning
  time
  temperature

## Slide 48: Wildlife and animal management
As a result of incidents of foodborne illness linked to raw agricultural foods and produce, FSMA also includes mandatory safety standards for produce and as a result is raising the bar on practices in the produce sector..
Limit access to production area
Monitor for evidence of animal presence in production area
Train employees

## Slide 49: Four major concerns on the FDA /USDA Priority Watch: the “Four W’s”
Water:
  pre-harvest and
  postharvest
Waste:
  manure, compost, biosolids
  feeding and grazing operations
Wildlife
Workers

## Slide 50: Sanitation and postharvest handling
Glove and apron policies
Clean and sanitize
  Harvest containers
  Equipment
Currently, whole fresh fruits and vegetables are exempt from legally required implementation of GMPs, but the focus on sanitation practices is good for reducing food safety risks in fresh produce operations. Adopting good postharvest practices will not only reduce food safety risks, but also contribute to maintaining produce quality and reducing postharvest decay.
To understand what risks may be present, an assessment of the packing and produce handling area should be completed. Any surface that the produce touches may serve as a source for contamination. Such surfaces include equipment, belts, rollers, brushes, tables, bins, sinks, tools, and even the hands of workers. Surfaces that contact produce must be able to be easily cleaned and preferably, sanitized.

## Slide 51: The concept of “zones” in GAPs /GHPs
Areas within the packing and handling area can be broken into zones to help determine the likelihood of direct contact with the produce you are handling.
Zone 1: Direct food contact surfaces such as conveyors, belts, brushes, rollers, sorting tables, racks, utensils, harvest/storage bins, and worker hands. This zone is the biggest concern because it has direct contact with the produce and if contaminated, could result in contamination of the entire crop.
Zone 2: Non-food contact surfaces that are in close proximity to the product, such as internal and external parts of washing or processing equipment such as sidewalls, housing, framework, or spray nozzles.
Zone 3: Areas inside of the packing area such as trash cans, cull piles, floors, drains, restrooms, forklifts, phones, and catwalks or storage areas above packing areas.
Zone 4: Areas outside of or adjacent to the packing area such as loading docks, warehouses, manure or compost piles, and livestock operations.

## Slide 52: Transportation
Cleaned
Covered
Checked prior to load/unload
Temperature monitored

## Slide 53: Traceability
Trace product one step, forward and backward
Date of harvest/pack date
Field identification
Worker identification
Maintain records

## Slide 54: Growers are GAP audited
Required by some buyers
Enhances marketability
Good business practice
To verify GAPs
  Ask if GAP audited
  Grower self-audit
  Visit farm, use checklists

## Slide 55: GAP resources
USDA GAP Audit Program http://www.ams.usda.gov/AMSv1.0/gapghp
Iowa State University checklist for Retail Purchasing of Local Produce https://goo.gl/y3pZeG
Penn State University http://extension.psu.edu/food-safety/farm
University of California Davis GAPS http://ucfoodsafety.ucdavis.edu/Preharvest/
Good Agricultural Practices (GAP) & Good Handling Practices (GHP)
  https://www.ams.usda.gov/services/auditing/gap-ghp
USDA Aligns Good Agricultural Practices Audits with FDA Food Safety Rule, Alignment Advances Food Safety Practices, Streamlines Regulatory Requirements https://goo.gl/ahh5zQ
Auburn researchers find food safety gaps at ‘local’ farms https://goo.gl/XnsAho

## Slide 56: GAP/GHP challenges
The focus of GAPs and GHPs is on fresh produce
Produce is food often consumed raw or minimally processed
The detection of pathogens prior to sale is very difficult
Sanitizing contaminated produce is very difficult
Product benefits
Benefits of consuming fresh produce far outweigh the risks
Food safety risks can be minimized

## Slide 57: The importance of GAP/GHP training to ensure food safety
Prevention of contamination is the single most important control factor to enhance food safety.
The key to preventing contamination is education.
It is not a one-size-fits-all | Washing does not solve the problem for some commodities that cannot be washed

## Slide 58: Discussion 2
Due by midnight EST on September 12, 2021:
Please read “The Jungle” by Upton Sinclair (1906) available as:
  a free eBook via Project Gutenberg at: goo.gl/rKZ5hd
  a free audio book via LibriVox at: https://bit.ly/3ju7uet
Discussion in 250-300 words:
Do you see a parallel to The Jungle in today's food production environment?
If yes, explain why. Use specific examples from the text or from your readings elsewhere to substantiate your stance. Remember to include citations.
If you do not believe there are parallels, substantiate your position meaningfully with citations.
Be sure to first declare your position on this matter. Then, explain clearly with substantiation and relevant citation. Use paragraphs and bullet points to separate different points and make your note easier to read and understand. Citations are not part of the total word count.

## Slide 59: Assignment 1: A critical review of a documentary
Due by midnight EST on September 26, 2021:
Watch the documentary Food Inc. The movie may be found free online at: https://vimeo.com/31813990
Although the documentary is more than a decade old, its narrative continues to be relevant in conversations happening currently about food production practices in the United states.
Write a critical review of the documentary in 250-300 words. Point out at least 5 blatant GMP or GAP/GHP errors in the documentary.
Ensure your submission has a clear bullet point list of the 5 or more GMP or GAP / GHP violations that you observed along with a sentence or two to explain. Substantiate with proper citation. Post in Assignment 1 in Module 2 Discussions
Be sure to review your fellow classmates’ posts with meaningful comments and suggestions.

## Slide 60: Checklist
Reading
Review lecture notes
Review FDA GMPs: http://goo.gl/KTpnQ3
Review USDA GAPs and GHPs: http://goo.gl/lV4Nbq
Virtual session:
7 pm CST on September 7, 2021 : https://zoom.us/j/93663364141 | Meeting ID: 936 6336 4141
Discussion 2
Do you see parallels to The Jungle in the food manufacturing sector today? Due midnight EST on September 12, 2021.
Assignment 1
A critical review of the documentary Food Inc. Due midnight EST on September 26, 2021.